## Slide 1: OS Fingerprinting and Tethering Detection in Mobile Networks
Yi-Chao Chen
The University of Texas at Austin
Joint work:
Yong Liao‡, Mario Baldi‡, Sung-Ju Lee‡, Lili Qiu†
Narus Inc. ‡, The University of Texas at Austin†

## Slide 2: Mobile OS Fingerprinting
Problem statement
  Infer what operating system a device is running by analyzing the packets it’s generating.
  Tethering detection: identify mobile devices which are sharing the Internet access
?
?
?
Notes: The number of mobile devices will exceed the world’s population by 2015.
mobile data traffic last year was nearly 18 times the size of the entire global Internet in 2000

## Slide 3: Importance
Tethering detection
  Billing for shared access in mobile networks
Security
  Policy enforcement in enterprise networks
Notes: Tethering:
tethering allows sharing the Internet connection of the phone or tablet with other devices such as laptops.
At&t policy for tethering
Knowing OS can launch attack – known security hole in iOS SSH
Allow malicious to access your phone

## Slide 4: Existing Works
Application
HTTP user agent [P0f], DHCP options [Satori]
Transport
Network
IP TTL, ID, dest address [P0f, PAM04]
Link
802.11 MAC fields, SSID, frame size [MOBICOM07]
TCP handshake, timeout, MTU, flags, init seq. number [P0f, NMap, VEYSET02, PAM04, RAID03], TCP Timestamp [INFOCOM99, IMW02]
Notes: Well known tool P0f: dynamics in TCP handshake and IP flags usage
Some other finds maximal transmission unit in TCP syn packet are different across OSes

## Slide 5: Limitation of Existing Works
Existing works focus on the Internet traffic
Mobile networks impose new challenges:
  Dynamic frequency due to power saving
    Clock skew, boot time estimation, …
  Short connections
    TCP flavors, initial sequence number, …
  Features might have changed in mobile OSes
    TCP MTU, IP flags, …
Notes: Clock frequency has been successfully and widely adopted in identifying NAT hosts, routes, …
but not in mobile networks due to dynamic frequency
clock skew, one of the prominent metrics used for device finger printing identified in the previous works doesn't work well for mobile devices.

## Slide 6: Approach
Identify features to fingerprint mobile device OSes
Detect tethering
  Clock frequency stability, boot time estimation
  IP Time-to-Live, ID Monotonicity
  TCP timestamp option, window size scale option, timestamp monotonicity
Combine multiple features
Quantify the performance
  Individual and combined features
  OS fingerprinting and tethering detection
Notes: All identify useful
Which are new
Which are changed (how)

## Slide 7: Dataset
Lab trace
  56 mobile user traces
    14 Android phones and tablets traces
      Samsung Galaxy S5, HTC Ones, HTC Inspire phones, Google Nexus 10 tablet
    10 iOS traces
      iPhone 4s, iPhone5s, iPad 2, iPod Touch
      iOS 5.1.1, iOS 6.1
    32 Windows laptops traces
      running Windows XP or Windows 7
  Each capture lasts 10~30 minutes

## Slide 8: Other Datasets
Trace | Time | Duration | # IPs
Lab Trace | Oct. 2013 | 2 hours | 56
SIGCOMM08 Trace | Aug. 2008 | 1 day | 223
OSDI06 trace | Nov. 2006 | 1 day | 292

## Slide 9: Features
Clock Frequency
  The frequency is stable in Android and Windows,
  but vary over time in iOS devices
High clock frequency std. suggests iOS
Notes: See this figure, it’s reasonable to …

## Slide 10: Features
IP ID Monotonicity
  Android:
    Some devices completely randomize the IP IDs
    Some periodically reset to random values.
  Windows: IP ID consistently increase monotonically
  iOS: randomize the IP ID of each packet
High violation ratio suggests iOS;
low violation ratio suggests Windows.
Notes: The identification field in the IP header is primarily used in IP de-fragmentation.

## Slide 11: Features
TCP Timestamp Option
  iOS and Android have TCP TS Option,
  but Windows doesn’t
Low ratio of TCP TS option suggests Windows.
Notes: The TCP timestamp option is used for measuring round trip time and protecting against wrapped sequence numbers.

## Slide 12: Features
IP Time-To-Live
TCP Window Size Scale Option
Boot time estimation
Notes: Refer to the paper for details

## Slide 13: Combining Features
Probability of finding feature fi in all traffic
Probability of finding feature fi in OSx’s traffic
Probability of being OSx
No single feature works in all scenarios
Naïve Bayes classifier
Notes: Why independent
it still works, we can remove the assumption if we have larger dataset

## Slide 14: Tethering Detection
Apply the same technique for tethering detection.
Features which identify mobile devices
  IP Time-To-Live
  TCP timestamp monotonicity
  Clock frequency
  Boot time estimation
  Multiple OSes

## Slide 15: Evaluation – Single Feature
No single feature identifies all OSes accurately.
Notes: Precision: the fraction of identified OS are correct
Recall: the fraction of the OS that are correctly identified

## Slide 16: Evaluation – Combing Features
Combining all features yields the best result.

## Slide 17: Evaluation – Tethering Detection
Combining all features also yields the best result in tethering detection.

## Slide 18: Conclusion
Contributions
  Identify new features for mobile OS fingerprinting and tethering detection
  Develop a probabilistic scheme that combines multiple features
Evaluate the individual and combined features
  Combing multiple features yields the best performance
  OS fingerprinting: 100% precision, 80% recall
  Tethering detection: 79%-89% recall when targeting 80% precision
Notes: Through our preliminary result,
This is an initial study, we
There are still tasks remains ..

## Slide 19: Thank You!
yichao@cs.utexas.edu

## Slide 20: Backup Slides

## Slide 21: Mobile OS Fingerprinting
Notes: The number of mobile devices will exceed the world’s population by 2014.
mobile data traffic last year was nearly 18 times the size of the entire global Internet in 2000

## Slide 22: Features
IP Time-To-Live (TTL)
  Windows: 64 or 128
  iOS and Android: 64

## Slide 23: Features
TCP Window Size Scale Option
  iOS: 16
  Windows and Android: 2, 4, 64, or 256
Notes: This option allows TCP client and server to negotiate and use a larger window size

## Slide 24: Evaluation – Comparing Classifiers
Probability based classifier outperforms other classifiers by 5~21% in F1-score measurement.