## Slide 1: SaDiF: Spoofing Attack on BLE Direction Finding Based Localization System
MobiHoc 2025
Runting Zhang, Yijie Li, Dian Ding, Hao Pan, Yongzhao Zhang, Xiaoyu Ji, Jiadi Yu, Guangtao Xue, Yi-Chao Chen
Notes: Good afternoon, everyone. My name is Runting Zhang from Shanghai Jiaotong University. Today I’ll be presenting our work: “SaDiF: Spoofing Attack on BLE Direction Finding Based Localization System.”

## Slide 2
BLE Direction Finding Feature
Indoor Navigation
Autonomous Guided Vehicles
Asset Tracking
Official standard for BLE localization
Popular Angular-based method
High Accuracy: submeter-level
AoA Method in Direction Finding
Notes: BLE Direction Finding was introduced in Bluetooth 5.1 and is now widely used in asset tracking, logistics, and smart factories for applications including indoor navigation, autonomous guided vehicles.
As an official standard, it enables a high-accuracy, sub-meter level localization performance.

## Slide 3
Motivation: Security Issue
BLE 5.1 Locator
AoA
Direction Finding Packet
Localization Result
BLE 5.1 Tag
Attacker
Jamming Attack
Man-in-the-Middle Attack
Faked Location
Localization systems are becoming the Prime Targets for malicious actors.
Package Loss
Property Damage
Is BLE Direction Finding Safe Enough?
Notes: However, as localization systems become more critical, they also become prime targets for attackers.
Considering a simple model of direction finding system,
an attacker may conduct a jamming attack to disable the localization function, causing serious logistics issues including package loss,
or manage to spoof the positioning result with a Man-in-the-Middle Attack, which may lead to significant property damage.
The question is now raised: is BLE Direction Finding really safe enough?

## Slide 4
BLE Direction Finding Process
RF Signal Transmission
Channel Sync
CTE Info Alignment
CTE Transmission
CTE Signal Sampling
Antenna Switching
AoA/AoD Estimation
Post Filtering
IQ Sampling
CFO Elimination
Angular Computation
Constant Tone Extension (CTE): Key Component
Notes: Let’s briefly look at how BLE Direction Finding works. There are mainly three parts: RF Signal Transmission, CTE Signal Sampling, and angular Estimation.
The key component is the Constant Tone Extension (CTE)—a segment of the signal used for phase sampling. By switching antennas and sampling the phase difference, the locator finally estimates the angle of arrival.

## Slide 5
CTE Structure and Transmission
Target
Locator
…
Guard Period
（4）
Reference Period
（8）
Switch
slot
Sample
Slot 1
Switch
slot
Sample
Slot 2
Switch
slot
Sample
Slot 74
…
CTE Format: 1 switching and sampling slots
ADV_EXT_IND
Advertising
AUX_ADV_IND
Ext Adv
CTE
AUX_SYNC_IND
CTE Info
Periodic advertising
CTE
AUX_SYNC_IND
CTE Info
……
Attacker may spoof the positioning result by Injecting the CTE period!
Notes: The CTE is transmitted between target and locator with a series of packets following the BLE periodic advertising.
Given the CTE Info segments, locator knows the exact CTE format and determine its corresponding antenna switching and sampling.
But since this process lacks authentication, Attacker may spoof the positioning result by Injecting the CTE period!

## Slide 6
SaDiF Illustration
AoA Localization
Trajectory
CTE
BLE packet
CTE
BLE packet
CTE
BLE packet
BLE 5.1
Tag
Notes: Now take a look at our SaDiF. In a logistics scenario relying on direction finding localization system,
Locators receiving the BLE packets with CTEs from tag, estimating the AoA and finally sending back the position of targets,
Autonomous Guided Vehicles or robots then plan its trajectory based on the given results.

## Slide 7
Injection Area
SaDiF Illustration
x
CTE
x
CTE
x
CTE
？
Wrong Trajectory
CTE
BLE Injection
BLE 5.1
Tag
Notes: Here, we propose SaDiF, in a certain injection area,
the attacker conducts the spoofing attack that injects malicious phase shifts during the CTE transmission,
misleading the locator into reporting a wrong trajectory of the victim device.

## Slide 8
Threat Model
Assumptions
Objectives
Victim: Users or Administrators of the BLE Direction Finding Localization System.
Goal: Manipulate the localization result of victim and create a misleading and continuous trajectory.
Attacker’s Capabilities:
  Access Locations of victim & locator
  Higher TX power than victim
  Antenna Array Structure
Attacker’s Restrictions:
  No Physical Access to any device in localization system
  Cannot Tamper with BLE Standard
  Limited Attacker’s Location
Notes: Our threat model defines the victim as Users or Administrators of Direction Finding System.
The attacker managed to Manipulate the localization result of victim and create a misleading and continuous trajectory.
The assumption of attacker includes the ability to: Access Locations of victim & locator; transmit RF signal with Higher power than victim; and acquire the Antenna Array Structure
The attacker is prohibited to: make any Physical Access to any device in localization system; Tamper with BLE Standard; and move its device to arbitrary places

## Slide 9
Challenges
Improve the Concealment of Attack, hard to detect
Maintain a Continuous and Deterministic Spoofing Path
Enhance the Attack Robustness against Hardware Imperfections
Notes: We faced three main challenges:
Bypassing existing defenses
Maintaining a continuous and deterministic spoofing path and
Ensuring robustness against hardware imperfections

## Slide 10
SaDiF Design
RF Signal Transmission
Channel Sync
CTE Transmission
CTE Info Alignment
CTE Signal Sampling
Antenna Switching
IQ Sampling
AoA Estimation
CFO Elimination
Angular Computation
Post Filtering
CTE Transmission
CFO Elimination
Wrong
CFO Est.
Angular Computation
Manipulated
AoA
Notes: Let’s go back to the direction finding process to reveal the design of Sadif.
We aim to spoof the original CTE transmission,
Resulting in a wrong CFO estimation,
And finally a manipulated AoA output.

## Slide 11
SaDiF Design
RF Signal Transmission
Channel Sync
CTE Transmission
CTE Info Alignment
CTE Signal Sampling
Antenna Switching
IQ Sampling
AoA Estimation
CFO Elimination
Angular Computation
Post Filtering
Manipulated
AoA
CTE-based Signal
Injection
C1
Attack Signal Generation
Phase Shift Filtering
C2
Injection Timing Optimization
C3
Wrong
CFO Est.
Notes: SaDiF works in three stages: First, we eavesdrop on BLE packets to sync with the victim.
Then, we generate an attack signal with a carefully filtered phase shift. Finally, we inject the signal during the CTE reference period, which leads to a wrong AoA estimation.
Following, I’ll show some design details of our system to deal with mentioned challenges.

## Slide 12
Challenge 1: Guarantee Attack Concealment
Predict Time and Channel for following packets
Decode Parameters indicating the CTE Format
Signal Injection Attack on CTE
No interference on the packet PDU
Preamble still comes from victim
Undetectable by common physical-layer detection mechanisms!
Preamble
Header
CRC
CTE
CTE Info
AUX_SYNC_IND
structure
AUXPtr
PDU
Notes: To firstly guarantee the concealment of our attack, we focus on the packet structure of AUX_SYNC_IND with CTE.
After decoding its PDU for segments AUXPtr and CTE Info, the attacker can Predict Time and Channel for following packets
Also acquiring Parameters indicating the CTE Format,
Which is essential for the Signal Injection Attack on CTE period
On the other hand, such injection ensures that Preamble still comes from victim,
And No interference on the packet PDU,
proving that it’s Undetectable by common physical-layer detection mechanisms, which rely on physical-layer features like packet preamble detection or RSSI deviation to detect spoofing.

## Slide 13
Locator
Attacker
Target
ADV_EXT_IND
AUX_ADV_IND
AUX_SYNC_IND
AUX_SYNC_IND
AUX_SYNC_IND
SYNC “Established”
Signal Eavesdrop
CTE-based Signal Injection
. . .
t
t
Attack Starts
Attack Works
CTE
AOA √
Fake AOA ×
injected CTE
CTE
AOA √
Notes: In detail, attack starts with a signal eavesdropping. Attacker eavesdrops the prepended BLE packets to synchronize with the target’s periodic advertising.
The synchronization is considered “established” when attacker successfully receives an AUX_SYNC_IND packet with CTE.
Attack finally works when CTE-based Signal Injection is conducted on the next AUX_SYNC_IND packet.

## Slide 14
Challenge 2: Maintain Attack Continuity
Reference Period(8μs)
Switch Slot
Smpl Slot1
Switch Slot
Smpl Slot2
Switch Slot
Smpl Slot3
Switch Slot
…
Time
Phase
Standard CTE (All 1s)
Smpl Slot74
. . .
Notes: Next, the second challenge of attack continuity comes from the angle estimation process.
When sampling a standard CTE, the CFO is estimated by reference-period samples.
Virtual antenna is aligned to finally derive the phase difference for following angular algorithm.
But considering the injected CTE,
Next, the second challenge of attack continuity comes from the angle estimation process.
When sampling a standard CTE, the CFO is estimated by reference-period samples.
Virtual antenna is aligned to finally derived the phase difference 𝝓_(𝟏→𝟐) for following angular algorithm.
But considering the injected CTE,

## Slide 15
Challenge 2: Maintain Attack Continuity
Reference Period(8μs)
Switch Slot
Smpl Slot1
Switch Slot
Smpl Slot2
Switch Slot
Smpl Slot3
Switch Slot
…
Time
Phase
Injected CTE
Smpl Slot74
. . .
Linear Phase Difference
Susceptible to Interference
Notes: We inject malicious phase shifts to the CTE reference-period signal,
Leading to a wrong CFO estimation result
And the corresponding manipulated phase difference (phi prime from 1 to 2)
However, the additional phase difference is linearly limited, which makes the output AoA Susceptible to Interference
We inject malicious phase shifts to the CTE reference-period signal,
Leading to a wrong CFO estimation result
And the corresponding manipulated phase difference 𝝓_(𝟏→𝟐)
However, the additional phase difference is linearly limited, which makes the output AoA Susceptible to Interference

## Slide 16
Attack Signal Generation
We introduce the Phase Shift Filtering algorithm to:
  Verify whether the manipulated AoA result is vulnerable to interference
  Filter the appropriate additional phase shift sets
  Select the expected phase shift for attack signal generation
Phase Shift Filtering Iteration
Notes: To maintain AoA continuity and avoid random jumps in positioning,
we designed our attack signal generation with a Phase Shift Filtering algorithm. It simulates the MUSIC spectrum, verifies the manipulated AoA result and filters out unstable phase shifts, ensuring the spoofed trajectory is smooth and believable.

## Slide 17
Challenge 3: Avoid Jitter Effect
Reference Period(8μs)
Switch Slot
Smpl Slot1
Switch Slot
Smpl Slot2
Switch Slot
Smpl Slot3
Switch Slot
…
Smpl Slot74
Guard Period(4μs)
Time ()
Jitter effect
Ideal injection
Delayed injection
Insufficient Covering
Unexpected Influence on Switching Samples
Notes: The last challenge of Hardware imperfection, or hardware jitter can cause timing errors, leading to unstable injection.
Considering an ideal injection that perfectly covers the CTE reference period,
Real-case injection may be delayed due to jitter effect,
Causing insufficient covering of reference-period samples,
And more seriously, unexpectedly influence the IQ samples among antenna switching, causing uncontrolled AoA outputs.

## Slide 18
Injection Timing Optimization
Reference Period(8μs)
Switch Slot
Smpl Slot1
Switch Slot
Smpl Slot2
Switch Slot
Smpl Slot3
Switch Slot
…
Smpl Slot74
Guard Period(4μs)
Ideal injection
Delayed injection
Time ()
Timing optimization
Jitter effect
Notes: So, we introduced an Injection Timing Optimization mechanism that shifts the transmission time slightly to maximize coverage of the reference period and minimize interference.
The optimized timing can be derived by solving this optimization problem.
So, we introduced an Injection Timing Optimization mechanism that shifts the transmission time slightly to maximize coverage of the reference period and minimize interference.
The optimized timing 𝑡_𝑜𝑝𝑡 can be derived by solving this optimization problems.

## Slide 19
Experiment Setup
Attacker’s Devices
Direction Finding Locator and Server
COTS Tags
Direction Finding Target (Victim)
Tag
Server
Laptop
USRP
Locator
Notes: We implemented SaDiF using a USRP N210 as the attacker,
and commercial BLE tags as victims
And we use a Silicon Labs Pro Kit with antenna array as the locator,

## Slide 20
In-Lab Scenario
Real Logistics Scenario
Experiment Setup
Attacker
Victim
Locator
Server
Attacker
Victim
Victim
Locator
Notes: Tests were conducted in both lab and real logistics environments.

## Slide 21
Performance
Attack on Still Point
Average Localization Deviation: 0.199m
Notes: For stationary targets, SaDiF achieved an average localization deviation of only 0.199 meters, successfully spoofing the location to a controlled false point.

## Slide 22
Performance
Attack on Trajectory
Average Localization Deviation: 0.250m
Notes: For moving targets, SaDiF still performed well, with an average deviation of 0.250 meters, creating a smooth and misleading trajectory.

## Slide 23
Conclusion
Proposed SaDiF that exploits the inherent vulnerabilities of CTE phase sampling process in BLE Direction Finding to mislead existing localization systems, reporting continuous and incorrect trajectories.
  - For other system details, including Detailed Algorithms, Full Evaluation Results and Countermeasures, please check our paper for more information.
Notes: In summary:
Our Proposed SaDiF exploits the inherent vulnerabilities of CTE phase sampling process in BLE Direction Finding to mislead existing localization systems, reporting continuous and incorrect trajectories.
For other system details, please check our paper for more information.

## Slide 24
Thank You
Notes: Thank you for your attention.

## Slide 25
Following
are backups

## Slide 26
Existing Defenses
Physical-Layer Defense
Existing defenses (identifications) against BLE spoofing attack exploit the unique Physical-Layer Feature of the BLE devices (e.g. preamble detection, RSSI deviation).
BlueID (Clock Skew Estimate)
BlueShield (RSSI Monitor)
Is BLE Direction Finding Safe Enough?
Notes: To counter these common attacks, existing defenses rely on physical-layer features like packet preamble detection or RSSI deviation to detect spoofing.
Among them, BlueID estimated the clock skew by comparing the phase pattern in received preamble. BlueShield monitored the RSSI and identify malicious user with abrupt RSSI change.
But is BLE Direction Finding really safe enough?
[Fig. 4. Preamble detections separated based on the GHT shown in Fig. 3.
Figure 4: Observed RSSI values under spoofing attacks (with typical channel interference). ]

## Slide 27
Micro-benchmarks
Notes: 备用

## Slide 28
Impact of Factors
Notes: 备用